## Slide 1
KMOU Division of Marine System Engineering
Introduction to
Internal Combustion Engine

## Slide 2: Lesson content for each week
Ch0_Introduction to the Class | Ch6_Piston Fittings and Crankshaft
Ch1_Overview of the Internal Combustion Engine | Ch7_Lube Oil System
Ch2_Thermodynamics and Compressed Air System | Ch8_Cooling Water System
Ch3_Marine Fuels and Internal Fuel Oil System | Ch9_Introduction to the Main Engine
Ch4_Intake and Exhaust System | Ch10_Alternative Fuels and Alternative Fuel Systems
Ch5_Turbocharger | Ch11_Environmental Regulations and Exhaust Gas Aftertreatment Systems
Midterm | Ch12_Tools, Apprentice Engineer Duties, and Career Direction
 | Final Exam

## Slide 3: What is Turbocharger (T/C)?
Most of the G/E turbochargers used on ships are made by ABB.
Therefore, this chapter explains ABB's T/C.
T/Cs are intended for turbocharging internal combustion engines.
The T/C is used to generate the volume of air and the charging pressure required to operate the engine.

## Slide 4: Turbocharger (T/C)
The T/C is a turbomachine consisting of the following main components:
O turbine
O compressor
These are mounted on a common shaft.
The exhaust gas from the diesel or gas engine flows through the gas inlet casing (9) and nozzle ring (8) to the turbine (7).
The turbine (7) uses the energy contained in the exhaust gas to drive the compressor wheel (11). The compressor draws in fresh air, compresses it and then forces it into the engine's cylinders.
8
Nozzle ring

## Slide 5: Turbocharger (T/C)
Nozzle ring
It is located just before the exhaust gas enters the turbine wheel.
The flow of exhaust gas is accelerated through the nozzle vane (blade) and guided to the turbine blade at the optimal angle of incidence.
It converts the pressure energy of the exhaust gas into kinetic energy to increase turbine efficiency.
8
Nozzle ring
Each of them is turbine blade
The nozzle increases the velocity of the fluid by making the outlet cross-sectional area smaller (contracting) than the inlet.
It is called a nozzle ring because it has multiple nozzles in a ring shape.
Each of them is nozzle vane (blade)
Exhaust gas flow
Exhaust
gas flow

## Slide 6: Turbocharger (T/C)
Bernoulli’s equation
Continuity equation
V: Volume
v: Velocity

## Slide 7: Turbocharger (T/C)
This is just an animation to illustrate the exhaust gas passing through the nozzle ring to the turbine wheel (left) and the fresh air being compressed by the compressor wheel (right).
Not in marine T/C
Not in marine T/C
Exhaust side
Exhaust side
Intake air side
Intake air side

## Slide 8: Turbocharger (T/C)

## Slide 9: Turbocharger (T/C)
To the funnel
Suction outside air
Turbine side of T/C
Compressor side of T/C
Turbocharger

## Slide 10: Turbocharger (T/C)
Intake
valve
Exhaust
valve
Piston
Exhaust manifold
Turbocharger
Air cooler
Turbine
Compressor

## Slide 11: Turbocharger (T/C)
The exhaust gas escapes into the ambient air through the exhaust gas pipe, which is connected to the gas outlet flange (6).
The air, which is necessary for operation of the diesel or gas engine and which is compressed in the turbocharger, is drawn into the compressor wheel (11) through the suction branch or filter silencer or through an axial suction pipe. It then passes through the diffuser (2) and leaves the turbocharger through the outlet on the compressor casing (1).
2
M/E
4 G/Es

## Slide 12: Turbocharger (T/C)
Diffuser
It is located between the compressor wheel outlet of the compressor and the compressor housing.
It converts the kinetic energy of the high-speed air exiting the compressor wheel into static pressure by slowing it down. In other words, the main pressure-increasing section of the compressor is the diffuser.
It increases the compressor discharge pressure to supply more air to the engine.
2
The diffuser has the same arrangement of vanes as the nozzle ring, with the outside being wider and the inside being narrower.
However, in the case of the nozzle ring, the exhaust gas enters from the outside, so the velocity increases, and in the case of the diffuser, the intake air exits from the inside to the outside, so the pressure increases.

## Slide 13: Turbocharger (T/C)
The rotor runs in two radial bearings (4/5) which are located in the bearing flange between the compressor and the turbine. The axial thrust bearing (3) is located at the compressor end.
The radial bearings are connected to a central lubricating oil duct which is fed with oil from the engine's lubricating oil circuit. The oil outlet is always at the lowest point of the bearing casing (10).

## Slide 14: Lubricant flow in the Turbocharger (T/C)

## Slide 15: Turbocharger (T/C)

## Slide 16: Turbocharger (T/C)
Speed measurement
A speed measuring system permits continuous monitoring of the turbocharger speed.

## Slide 17: Components of T/C

## Slide 18: Components of T/C
Compressor casing
V-clamp
V-clamp

## Slide 19: Components of T/C

## Slide 20: Components of T/C
Compressor casing
O-ring
Wall insert
V-clamp
Diffuser
O-ring
O-ring
Bearing flange
Positioning
pin

## Slide 21: Components of T/C
Bearing casing
Bearing casing
V-clamp
Nozzle ring

## Slide 22: Radial clearances N and R for T/C
These are the theoretical values of the radial clearance between the compressor wheel and the wall insert and / or turbine wheel and the gas outlet flange.
The minimum and maximum values result from the manufacturing tolerances of the compressor wheel and turbine wheel or the wall insert and gas outlet flange.
N1 and N2 as well as R1 and R2 are each measured at the same time using two feeler gauges.

## Slide 23: Radial clearances N and R for T/C
To measure N1 and N2, the feeler gauges must be pushed between the wall insert and the compressor wheel free of play, in each case above and below.
To measure R1 and R2, the feeler gauges must be pushed between the gas outlet flange and the turbine free of play, in each case above and below.

## Slide 24: Components of T/C
The mean values measured must be within the permissible values of the radial clearance N and R.
Clearances out of tolerance and excessively worn components can be the cause of serious damage to machinery and property.

## Slide 25: Components of T/C

## Slide 26
O-ring
Bearing casing
Partition wall
Nozzle ring
Verbusripp washer
Hexagon socket screw
Piston ring
Shaft
Orifice plate
Hexagon socket screw
Piston ring
Compressor wheel
Hexagon socket screw
Cup spring
Lock nut
Bearing cover
O-ring
Bearing bush
Thrust bearing
Thrust ring
Plain bearing bush
Safety ring
Bearing flange
O-ring

## Slide 27: Cleaning of T/C
Regular cleaning of the exhaust turbine is essential to ensure optimum engine operation using HFO as fuel.
Depending on the quality of the fuel used, particularly hard deposits can be formed on the nozzle ring in conjunction with high exhaust gas temperatures.
Heavily contaminated turbine components, in particular a contaminated nozzle ring, lead to deterioration in turbine efficiency. Reduced engine power and poorer efficiency are the result.
Under certain circumstances, even the omission of only one turbine washing cycle can lead to a build-up of carbon residues that can no longer be removed with the next regular cleaning process. The resulting need for an early turbocharger service increases the operating costs of the engine plant.
Contaminated nozzle ring of T/C

## Slide 28: Cleaning of T/C
Turbine cleaning
Generally, there are two different washing processes for cleaning the turbine: short-term and long-term washing. Which washing process to use depends on the turbocharger type.
In short-term washing, water is introduced into the turbine several times for a short time. This leads to temperature shocks which cause the dirt to flake off.
The cleaning effect of long-term washing is based on dissolving the dirt with water. Thus, the 10 minute cleaning time should ensure that all dirty surfaces are wetted with water and that dirt is dissolved.

## Slide 29: Cleaning of T/C
Despite regular turbine washing in compliance with the washing parameters, if the turbines and nozzle rings are dirty, manual cleaning of the components is necessary.
Chemical analyses show that usually deposits on turbines and nozzle rings are mainly oxidic vanadium compounds. If fuels with a high vanadium content are used, we recommend shortening the washing intervals.
Field experience and tests have shown improved cleaning results with the long-term washing procedure, therefore in case operators experience insufficient cleaning results with the short term water injection, ABB recommends changing to long-term washing.

## Slide 30: Dry cleaning of T/C turbine side

## Slide 31: Water washing of T/C turbine side
https://www.youtube.com/watch?v=vzn5oku3xOo

## Slide 32: T/C cleaning for compressor and turbine sides
Ball valve

## Slide 33: T/C cleaning for compressor

## Slide 34: T/C cleaning for compressor
Screw plug
Container
Valve activator
Pressurized air
Water
Operating state prerequisites for cleaning compressor with XC1
To be able to carry out a satisfactory cleaning process which has been tested and is recommended by ABB Turbocharging, the following prerequisites must be fulfilled:
1) Run engine at load from 50 … 85 %.
2) Start cleaning cycle according to following description Wet cleaning operation with XC1.

## Slide 35: T/C cleaning for compressor
Screw plug
Container
Valve activator
Pressurized air
Water
Operating state prerequisites for cleaning compressor with XC1
Operating the water pressure vessel
1) Remove the screw plug (X).
2) Fill the vessel with clean water.
3) Replace the screw plug.
4) Push the valve activator (Y) against the spring and hold it for 10 to 15 seconds until entire volume of water has been injected.
5) After cleaning, wait at least 5 minutes with the engine running to allow the turbocharger to dry.
6) The cleaning cycle may only be repeated after a stabilization period of at least 10 minutes has elapsed.

## Slide 36: T/C cleaning for compressor and turbine sides

## Slide 37: T/C system

## Slide 38: Troubleshooting for T/C
Notes: periphery : (어떤 범위의) 주변
adjacent : 인접한, 가까운

## Slide 39: Troubleshooting for T/C
Notes: sporadic : 산발적인, 이따금 발생하는
momentarily : 잠깐 (동안)
impair : 손상[악화]시키다

## Slide 40: T/C surging on G/E

## Slide 41: Troubleshooting for T/C

## Slide 42: Troubleshooting for T/C

## Slide 43: Troubleshooting for T/C

## Slide 44: Troubleshooting for T/C

## Slide 45: References
1) https://www.manualslib.com/download/2380893/Abb-Tps-50b01.html
2) https://www.manualslib.com/download/2258430/Abb-Tps48-F32.html
3) https://en.wikipedia.org/wiki/File:W%C3%A4rtsil%C3%A4_6L20.jpg
4) https://www.manuallib.com/download/2023-10-27/ABB%20%E6%B6%A1%E8%BD%AE%E5%A2%9E%E5%8E%8B%E5%99%A8%E6%93%8D%E4%BD%9C%E6%89%8B%E5%86%8C%20TPS44-H33%20HT588474.pdf
5) https://www.turbodynamics.co.uk/how-does-a-turbocharger-work
6) https://malwimarine.com/wartsila-6l20-complete-engine/
7) https://alsolmarine.ae/products/nozzle-ring
8) https://www.reddit.com/r/cars/comments/3v1c0z/animated_gif_of_a_turbocharged_engine/

## Slide 46: References
9) https://www.wartsila.com/encyclopedia/term/engine-room-arrangement
10) https://dir.indiamart.com/impcat/turbocharger-parts.html?biz=10
11) http://hyperphysics.phy-astr.gsu.edu/hbase/pber.html
12) https://www.youtube.com/watch?v=wykn-JTnacE
13) https://www.niddk.nih.gov/news/media-library/17826
14) https://megaturboss.com.mx/products/kit-gigante
15) https://zeppelin-cat.dk/wp-content/uploads/2025/06/M32-008.pdf
16) https://zeppelin-cat.dk/wp-content/uploads/2025/06/M32-008.pdf
17) https://ko.wikipedia.org/wiki/ABB_%EA%B7%B8%EB%A3%B9
18) https://convalve.eu/language/en/how-ball-valves-work/
19) https://www.youtube.com/watch?v=ARFYhjszrpk