## Slide 1
KMOU Division of Marine System Engineering
Introduction to
Internal Combustion Engine

## Slide 2: Lesson content for each week
Ch0_Introduction to the Class | Ch6_Piston Fittings and Crankshaft
Ch1_Overview of the Internal Combustion Engine | Ch7_Lube Oil System
Ch2_Thermodynamics and Compressed Air System | Ch8_Cooling Water System
Ch3_Marine Fuels and Internal Fuel Oil System | Ch9_Introduction to the Main Engine
Ch4_Intake and Exhaust System | Ch10_Alternative Fuels and Alternative Fuel Systems
Ch5_Turbocharger | Ch11_Environmental Regulations and Exhaust Gas Aftertreatment Systems
Midterm | Ch12_Tools, Apprentice Engineer Duties, and Career Direction
 | Final Exam

## Slide 3
Cooling
fresh water expansion tank

## Slide 4
Cooling
fresh water expansion tank

## Slide 5: Cooling fresh water expansion tank
Cooling water storage and replenishment function
Stores cooling water (fresh water) used to cool the engine. It replenishes cooling water lost to evaporation, leakage, etc. during operation.
Provides space for cooling water expansion (acts as an expansion tank)
When the engine is running, the cooling water heats and expands. The cooling fresh water expansion tank receives this expanded cooling water, maintaining stable cooling system pressure.
Cooling water degassing
During operation, air (gas) bubbles may form in the cooling water. The tank provides a space for this gas to separate and escape, preventing cavitation and ensuring circulation stability.
Maintains circulation pressure
Since the cooling water system is a closed circulation system, the tank acts as a head tank, maintaining a constant water head. This ensures stable inlet pressure to the pump.
Cooling water quality control
Cooling fresh water expansion tanks typically have chemical inlets, allowing the addition of corrosion inhibitors or alkalinity regulators to prevent corrosion and scale.

## Slide 6: Cooling fresh water expansion tank

## Slide 7: Cooling fresh water expansion tank

## Slide 8: Cooling water system (HiMSEN)
The engine has two cooling water circuits internally, which are low temperature (LT) system and high temperature (HT) system. Most of the elements of the circuits are modularized and directly mounted on the feed block.
The cooling water system is designed for using normal fresh water with corrosion inhibitor. Both the low and the high temperature system are cooled by fresh water.

## Slide 9: Cooling water system (HiMSEN)
The low temperature cooling water circulates by L.T pump and flows through charge air cooler and lubricating oil cooler internally.
L.T.W thermostat valve controls the water temperature by exchanging water with external circuit as shown in fig. 1.
The high temperature cooling water circulates by H.T pump internally and flows through cylinder head and water jacket (for cylinder liner) under normal operation. H.T.W thermostat valve controls the water temperature by exchanging water with external circuit.
charge air cooler

## Slide 10
O-ring
O-ring
Sleeve
Water guide jacket
O-ring
Sealing ring
Plug screw
O-ring
Sealing ring
Cooling water connection
O-ring
Sealing ring
Cylinder liner
O-ring
Flame ring
Water guide jacket
Sleeve
Washer
Hexagon screw

## Slide 11: Cooling water system (HiMSEN)
The two cooling water pumps are of a centrifugal type and are driven by the gear wheel at the free end of the engine.
These two pumps are identical, but one is for circulating high temperature cooling water and the other is for low temperature cooling water.
Sealing rings are provided to avoid leakage between water side and oil side in the pump housing.

## Slide 12: Cooling water system (HiMSEN)
The two thermostat valves for HT and LT water circuits respectively are mounted on the feed block of the engine.
They are of the wax element type and cannot be adjusted. The thermostat valve controls the flow direction of the cooling water depending on the water temperature in the engine block appropriately as shown in fig. 3.

## Slide 14: Cooling water system (HiMSEN)

## Slide 15: Cooling water system (HiMSEN)
Cooling water inlet pipe assembly
Cooling water outlet pipe assembly

## Slide 16: Cooling water system (HiMSEN)
L.O. cooler

## Slide 17: L.O. cooler

## Slide 18: Plate type heat exchanger (=Cooler)

## Slide 19: Plate type heat exchanger (=Cooler)

## Slide 20: Plate type heat exchanger (=Cooler)

## Slide 21: Plate type heat exchanger (=Cooler)

## Slide 22: Plate type heat exchanger (=Cooler)

## Slide 23: Plate type heat exchanger (=Cooler)

## Slide 24: Plate type heat exchanger (=Cooler)
In plate type heat exchangers, a rubber gasket is used to separate the two fluid flows.
However, rubber gaskets harden when exposed to heat for a long period of time, becoming less elastic and thus hindering the separation of the two fluids.
In particular, when the plate inside the plate type heat exchanger is disassembled for cleaning, the elasticity and damage of the gasket should be checked, and any problematic gaskets should be replaced with spare gaskets.

## Slide 25: Plate type heat exchanger (=Cooler)
After cleaning the plate, when assembling the plate exchanger, tighten the tightening nut in an X shape to ensure that the rubber gasket is evenly sealed throughout.
If you tighten one nut as tight as possible and then tighten the other nut as tight as possible, the rubber gasket will not seal evenly, causing leakage.

## Slide 26: Plate type heat exchanger (=Cooler)

## Slide 27: Plate type heat exchanger (=Cooler)

## Slide 28: Shell type heat exchanger (=Cooler)
The L.O. cooler of some generators uses a shell type heat exchanger.

## Slide 29: Air Cooler (HiMSEN)
Charge air cooler

## Slide 30: Air Cooler (HiMSEN)
Cooling water flows through the tubes and charged air from the turbocharger flows between the fins.
Accordingly, heat exchange occurs between the cooling water and the charged air, so that the charged air is cooled and supplied into the cylinder.
Charged air
Cooling water

## Slide 31: Air Cooler (HiMSEN)

## Slide 32: Cooling water treatment test
A cooling water treatment test is conducted to determine the current condition of the G/E's cooling water.
Based on the test results, chemicals are added to the cooling fresh water expansion tank to prevent corrosion and suppress scale caused by cooling water.
1) Nitrite test, 2) Chloride test, 3) pH test
Notes: Nitrite: 아질산염
Chloride: 염화물

## Slide 33: References
1) https://www.thermomegatech.com/products/
2) https://www.youtube.com/watch?v=nJEF5uO9o2g
3) https://www.youtube.com/watch?v=r-8vv3dQ1oc
4) https://www.youtube.com/watch?v=uEInVVcc6Sc
5) https://www.youtube.com/watch?v=_2xPxMPZV6I
6) https://www.youtube.com/watch?v=s5nJG0om8KY
7) https://www.sciencedirect.com/science/article/pii/S0142941816311643?via%3Dihub
8) https://www.alfalaval.my/products/heat-transfer/plate-heat-exchangers/gasketed-plate-and-frame-heat-exchangers/heat-exchanger/how-plate-heat-exchanger-work/

## Slide 34: References
9) https://nlmotoring.com/wheel-academy/how-to-tighten-lug-nuts/?srsltid=AfmBOooBJojGDbeolgqsz7mvjOOXO_OW6vSWCtFHcM_JrrFQFYmnjEUC
10) https://www.youtube.com/watch?v=Atz2XwcjZ48
11) https://www.youtube.com/shorts/2qQGLiCL4vo
12) http://generalcargoship.com/charged-air-cooler.html
13) https://muckymariners.com/app/meo-class-4-subjects/function-4b-meol/auxiliary-machines/11-heat-exchanger/heat-exchanger-2-5-types/
14) https://www.vrcoolertech.com/news/5-types-of-shell-and-tube-heat-exchangers-and-78264382.html
15) https://www.justdial.com/jdmart/Bangalore/Stainless-Steel-Heat-Exchanger-Suitable-for-Industrial-Applications-Flow-Rate-1200-Nm3hr-Maximum-Working-Pressure-10-bar/pid-2031869768/080PXX80-XX80-110315174638-U3S5

## Slide 35: References
16) https://www.youtube.com/watch?v=CNry-CKNkeM
17) https://www.wilhelmsen.com/product-catalogue/products/marine-chemicals/water-treatment-chemicals/cooling-water-treatment/
18) https://www.freyssinet.com/solution/build/expansion-joints/expansion-joints-road/