## Slide 1
KMOU Division of Marine System Engineering
Introduction to
Internal Combustion Engine

## Slide 2: Lesson content for each week
Ch0_Introduction to the Class | Ch6_Piston Fittings and Crankshaft
Ch1_Overview of the Internal Combustion Engine | Ch7_Lube Oil System
Ch2_Thermodynamics and Compressed Air System | Ch8_Cooling Water System
Ch3_Marine Fuels and Internal Fuel Oil System | Ch9_Introduction to the Main Engine
Ch4_Intake and Exhaust System | Ch10_Alternative Fuels and Alternative Fuel Systems
Ch5_Turbocharger | Ch11_Environmental Regulations and Exhaust Gas Aftertreatment Systems
Midterm | Ch12_Tools, Apprentice Engineer Duties, and Career Direction
 | Final Exam

## Slide 3: Thermodynamics
What is Thermodynamics?
Thermodynamics is a branch of physics which deals with the energy and work of a system.
It was born in the 19th century as scientists were first discovering how to build and operate steam engines.
Thermodynamics deals only with the large scale response of a system which we can observe and measure in experiments. Small scale gas interactions are described by the kinetic theory of gases.

## Slide 4: Zeroth Law of Thermodynamics
What is the “Zeroth Law of Thermodynamics”?
→ If two systems are each in thermal equilibrium with a third system, then the two systems are in thermal equilibrium with each other.
Notes: Thermodynamic equilibrium : 열역학적 평형

## Slide 5: First Law of Thermodynamics
What is the “First Law of Thermodynamics”?
→ Energy is neither created nor destroyed, it only changes form.

## Slide 6: Second Law of Thermodynamics
What is the “Second Law of Thermodynamics”?
→ The entropy of an isolated system always increases or remains constant. (Natural processes proceed in the direction of increasing entropy.)

## Slide 7: Third Law of Thermodynamics
What is the “Third Law of Thermodynamics”?
→ The entropy of a closed system at thermodynamic equilibrium approaches a constant value when its temperature approaches absolute zero.

## Slide 8: 4-stroke ICE (G/E)

## Slide 9: 4-stroke ICE (G/E)
This class (Internal Combustion Engine) will mainly cover the content for G/E.
Why this class mainly covers for G/E?
1) Most of the students for this class will be onboard soon as an apprentice engineer (A/E).
2) There must be a chance of attending maintenance works for G/E with 2nd engineer.
3) Most of the students for this class will be onboard as a 3rd engineer and then be 2nd engineer before finishing military service.
4) 2nd engineer is in charge of G/E.
5) There will not be the education for G/E after graduation of university. (In my experience, company did not teach for G/E and I had to study by myself when I was 3rd and 2nd engineer.)
6) Therefore, I hope all students get benefit from this class for the knowledge of G/E.
7) At the end of class, I will shortly introduce for M/E too.

## Slide 10: 4-stroke ICE (G/E)
There are several makers of G/E that you will encounter when boarding a ship.
Some of them are shown in below.
(S.Korea)
(Japan)

## Slide 11: 4-stroke ICE (G/E)
There are several makers of G/E that you will encounter when boarding a ship.
Some of them are shown in below.
(Japan)
(Germany)

## Slide 12: 4-stroke ICE (G/E)
There are several makers of G/E that you will encounter when boarding a ship.
Some of them are shown in below.
(Finland)
You will encounter the G/E of the five brands described above when you board the ship.
Most ships recently built in Korean shipyards and owned by Korean shipowners are equipped with HiMSEN engines.
As you may have noticed, the G/E of all brands looks similar.
As they look similar, the structure and operating mechanism of all G/Es are almost identical.
Therefore, if you fully understand the G/E of just one brand, you will have no problem understanding the G/E of other brands.

## Slide 13: 4-stroke ICE (G/E)
As explained in Chapter 1, G/E is divided into the Engine side and the Generator side.
The Engine side generates rotational force to the crankshaft through the reciprocating motion of the piston.
The Generator side uses the rotational power of the crankshaft to produce electricity from the generator.
A ship usually has 3 to 4 G/Es installed.
Engine
Generator
Generator Engine (G/E)

## Slide 14: 4-stroke ICE (G/E)
Imagine
a generator connected to a shaft instead of a propeller.
Engine side
Engine side
Generator side
Generator side

## Slide 15: 4-stroke ICE (G/E)
Since the generator side is probably covered in the class of "Marine Electrical and Electronic Engineering," this class (Internal Combustion Engine) only focuses on the engine side.

## Slide 16: Compressed Air System for G/E

## Slide 17: Marine air compressor
How does G/E start?
To answer this, you need to understand the Compressed Air System.
There are 2 to 3 air compressors installed on the ship, and they look like below.
Motor
Air compressor

## Slide 18: 4-stroke ICE (G/E)
The engine side of the G/E and air compressor have a similar structure.
The differences between the driving mechanisms of G/E and air compressor are as follows.
G/E creates a reciprocating motion of the piston by the explosive force from the combustion of air and fuel, which rotates the crankshaft, and a generator is connected to the crankshaft to produce electricity.
Energy flow

## Slide 19: Marine air compressor
An air compressor has a crankshaft connected to the shaft of a motor, and the rotational force of the motor creates a reciprocating motion of a piston, which compresses the air and produces compressed air.
Energy flow
Motor rotational power

## Slide 20: Marine air compressor
Compressed air produced by the air compressor is stored in air reservoir tanks for starting the M/E and G/E.
No. 1 air reservoir tank
No. 2 air reservoir tank
3 air compressors

## Slide 21: Air reservoir tank
The air reservoir tank is filled with compressed air, and there is condensed water at the very bottom of the tank, so the apprentice engineer usually opens the drain valve to drain it in the morning and at afternoon.
The reason for draining is that if moisture is mixed in the compressed air and flows into the M/E or G/E when they are started, there is a possibility that it will cause a damage and malfunction.
The actual air reservoir tank on a ship is not as small as the picture on the left, but is very large as shown in the picture on the previous slide.
The left one might be the auxiliary air reservoir tank .
Water drain valves
Clockwise: Valve close
Counterclockwise: Valve open

## Slide 22: Valve

## Slide 23
Oil&Water Separator

## Slide 24: Compressed Air System of G/E

## Slide 25: Compressed Air System of G/E

## Slide 26: Compressed Air System of G/E
The compressed air is continuously supplied from the starting air
receivers (30 bar) through a reduction station to the Compressed Air System of G/E.
1 atm = 1.01325 bar
atm = atmospheres

## Slide 27: Compressed Air System of G/E
The air starter is activated with a pneumatic 3/2 way solenoid valve (starting valve).
The air starter can be activated manually from the starting box on the engine, and it can be activated by remote control, manual or automatic.
When the starting valve is opened, air will be supplied to the drive shaft housing of the air starter.
(Pneumatic 3/2 way
solenoid valve)

## Slide 28: Compressed Air System of G/E
(Pneumatic 3/2 way
solenoid valve)

## Slide 29: Compressed Air System of G/E

## Slide 30: Compressed Air System of G/E
The air supply will - by activating a piston - bring the drive pinion into engagement with the gear rim on the engine flywheel.
(Pneumatic 3/2 way
solenoid valve)
Drive pinion
Engine flywheel
This animation illustrates the engagement of the air starter's drive pinion and the gear rim on the engine flywheel. On ships, air starter is driven by compressed air, not electricity.
Push
Drive pinion
Air starter
Gear rim

## Slide 31: Compressed Air System of G/E
Example of an air starter installed in a G/E
Engine flywheel
Drive pinion
Air starter
Gear rim of flywheel

## Slide 32: Compressed Air System of G/E
Drive pinion
Example of an air starter (turbine starter) installed in a G/E

## Slide 33: Compressed Air System of G/E
Exploded view of the air starter
Drive pinion
: Bearing
: O-ring

## Slide 34: Ball bearing

## Slide 35: Ball bearing

## Slide 36: Ball bearing

## Slide 37: Ball bearing

## Slide 38: O-ring

## Slide 39: O-ring

## Slide 40: O-ring
https://www.youtube.com/shorts/o-Qs2qcS4dU

## Slide 41: Compressed Air System of G/E
When the pinion is fully engaged,
the pilot air will flow to, and open the main starting valve, whereby air will be led to the air starter, which will start to turn the engine.
When the RPM exceeds approximately 110 (depends on G/E model), at which firing has taken place, the starting valve is closed whereby the air starter is disengaged.
(Pneumatic 3/2 way
solenoid valve)
Drive pinion
Engine flywheel
Turn

## Slide 42: Compressed Air System of G/E
The system is equipped with an emergency
starting valve which makes it possible to activate the air starter manually in case of a power failure.
The emergency starting valve is activated by means of a screw-driver or similar.
(Pneumatic 3/2 way
solenoid valve)
Drive pinion
Engine flywheel
Turn

## Slide 43: Compressed Air System of G/E
Example of an air starter installed in a G/E
Engine flywheel
Drive pinion
Air starter
Compressed air from starting valve
Main starting valve
G/E

## Slide 44: Compressed Air System of G/E
Starting air motor (=Air starter)

## Slide 45: Compressed Air System of G/E

## Slide 46: Compressed Air System of G/E

## Slide 47: Compressed Air System of G/E

## Slide 48: Compressed Air System of G/E

## Slide 49: Compressed Air System of G/E

## Slide 50: Compressed Air System of G/E

## Slide 51: Start & stop panel for G/E (HiMSEN)
‘START’ button on the control panel activates starting solenoid valve opened to supply compressed air into the starting air motor. Then, the pinion of the air starting motor is engaged with the gear rim of the engine flywheel and turns crankshaft of the engine.
Hence, when the engine rotating speed reaches predetermined speed, fuel oil is injected into the combustion chamber for self-rotating. Then, starting is completed and the pinion of the air starting motor is disengaged from the gear rim at predetermined speed.
Start
Stop
Start
Stop
It is located next to G/E.
It is located on the main switchboard in the engine control room.
Start

## Slide 52: References
1) https://www1.grc.nasa.gov/beginners-guide-to-aeronautics/zeroth-law-thermal-equilibrium/
2) https://www.grc.nasa.gov/www/k-12/airplane/thermo1.html
3) https://www1.grc.nasa.gov/beginners-guide-to-aeronautics/second-law-entropy/
4) https://en.wikipedia.org/wiki/Third_law_of_thermodynamics
5) https://www.chemistrylearner.com/laws-of-thermodynamics/third-law-of-thermodynamics
6) https://en.yna.co.kr/view/PYH20240129103500315
7) https://veig-bx.com/creating-a-powerful-new-identity
8) https://ko.wikipedia.org/wiki/%ED%8C%8C%EC%9D%BC:Hyundai_Heavy_Industries_logo_%28english%29.svg

## Slide 53: References
9) https://www.soar.hk/marinegenset4_en/
10) https://jamestroop.co.uk/partner/diahatsu/
11) https://www.yanmar.com/global/powergeneration/products/diesel_generators/
12) https://ancasta.com/yacht-services/yanmar-dealer/
13) https://www.maritimenetwork.dk/en/everllence/
14) https://www.tradekorea.com/product/detail/P358813/STX-Man-6L-23-30-H-marine-generator-set.html
15) https://www.everllence.com/
16) https://smiec.co.id/brand/

## Slide 54: References
17) https://loadbanks.com/man_diesel_turbo/
18) https://www.valantic.com/en/case-studies/aps-waysuite-at-man-es-production-planning-ai-optimized/
19) https://ko.wikipedia.org/wiki/%ED%8C%8C%EC%9D%BC:W%C3%A4rtsil%C3%A4_logo.png
20) https://www.indiamart.com/proddetail/wartsila-6l20-8l20-6r32-8r32-marine-engine-generator-21468731848.html?srsltid=AfmBOoqGrbLB1O_IaM-igeHRohnLyemvmJiopZJViot2mGX5l2TSdmov
21) https://medium.com/@Breadarose/what-is-the-lifespan-of-a-typical-diesel-electric-generator-f47cc962de17
22) https://kr.pinterest.com/pin/315392780158380877/
23) https://tenor.com/ko/search/ac-generator-gif-gifs
24) https://yesway.co.uk/smart-ships-generator-how-they-work-fail/

## Slide 55: References
25) https://www.csi-es.com/product/csi-ningdong-gn320-series-marine-diesel-generator-set-1500-2200kw/
26) https://wildonengineering.com.au/marine-compressor-factors-to-consider-for-seaworthy-performance/
27) https://marineprogress.com/marine-air-compressors/
28) https://us.fscurtis.com/product/ml-series/
29) https://www.marineinsight.com/tech/air-compressor/compressed-air-line-on-ships/
30) https://cdn1.shipserv.com/ShipServ/pages/profiles/200862/documents/MAN-L28-32H_CODE-BOOK_GALUAL.pdf
31) https://www.atosolenoidvalves.com/how-does-3-2-pneumatic-solenoid-valve-work.html
32) https://www.airmaxindia.com/3-2-way-single-solenoid-valves/

## Slide 56: References
33) https://in.pinterest.com/pin/584271751649916183/
34) https://www.ipu.co.uk/products/air-starters/
35) https://airstartersdirect.com/turbine-air-starters/st1060bi03r31s-2g/?srsltid=AfmBOootgZX8KfjmFq-SgP3sxLzXgxbJtX-HVnSim8YFqevmt2PxYHFO
36) https://khinzawshwecom.wordpress.com/wp-content/uploads/2018/05/instruction-manual-for-shina-xin-an-sas-430.pdf
37) http://kkthebest.com/pressure-vessel/service-control-air-reservoir/
38) http://www.komeco.net/bbs/board.php?bo_table=products01_e&wr_id=14
39) https://www.facebook.com/groups/2755620331372660/posts/3598232350444783/
40) https://www.youtube.com/watch?v=0cLcnudOJWg
41) https://unsplash.com/ko/s/%EC%82%AC%EC%A7%84/engine-room

## Slide 57: References
42) https://www.youtube.com/shorts/xfG1JyienUY
43) https://www.youtube.com/shorts/KzUHDCjN5OI
44) https://www.youtube.com/watch?v=gd3JaxileD8
45) https://www.youtube.com/watch?v=T53zdMvOPmE
46) https://www.youtube.com/shorts/o-Qs2qcS4dU
47) https://www.youtube.com/watch?v=aweDWuNkPw0
48) https://www.youtube.com/watch?v=kbjTQlkIho8
49) https://www.youtube.com/watch?v=3nq13KDcALg
50) https://www.youtube.com/watch?v=AhjyPhohbnU