## Slide 1
KMOU Division of Marine System Engineering
Introduction to
Internal Combustion Engine

## Slide 2: Lesson content for each week
Ch0_Introduction to the Class | Ch6_Piston Fittings and Crankshaft
Ch1_Overview of the Internal Combustion Engine | Ch7_Lube Oil System
Ch2_Thermodynamics and Compressed Air System | Ch8_Cooling Water System
Ch3_Marine Fuels and Internal Fuel Oil System | Ch9_Introduction to the Main Engine
Ch4_Intake and Exhaust System | Ch10_Alternative Fuels and Alternative Fuel Systems
Ch5_Turbocharger | Ch11_Environmental Regulations and Exhaust Gas Aftertreatment Systems
Midterm | Ch12_Tools, Apprentice Engineer Duties, and Career Direction
 | Final Exam

## Slide 3: 4-stroke ICE (G/E)
Inside the G/E cylinder, atomized fuel injected from the fuel injection nozzle and pressurized air supplied by the turbocharger are mixed and exploded, pushing the piston downward to reciprocate and generate rotational power.
The goal of this chapter is to learn about the fuel used on ships and the fuel supply system.

## Slide 4: Marine fuels
The fuels typically used on ships are as follows:
HFO : Heavy Fuel Oil
VLSFO : Very Low Sulfur (Sulphur) Fuel Oil
MDO : Marine Diesel Oil
MGO : Marine Gas Oil
LSMGO : Low Sulfur Marine Gas Oil

## Slide 5: Marine fuels
Fractional distillation of crude oil
Fractional distillation of crude oil
Notes: Remnant: : 남은 부분, 나머지
Fractional Distillation : 분별 증류(액체 혼합물을 가열하여 각각의 성분을 분리해 내는 방법)

## Slide 6: Marine fuels
Crude oil tanker
Crude oil
Yeosu complex
Ulsan complex

## Slide 7: Marine fuels
HFO (Heavy Fuel Oil):
HFO is a category of fuel oils of a tar-like consistency.
Also known as bunker fuel, or residual fuel oil, HFO is the result or remnant from the distillation and cracking process of petroleum.
For this reason, HFO contains several different compounds that include aromatics, sulfur, and nitrogen, making emissions upon combustion more polluting compared to other fuel oils.
HFO is predominantly used as a fuel source for marine vessel propulsion using marine diesel engines due to its relatively low cost compared to cleaner fuel sources such as distillates.
The use and carriage of HFO on-board vessels presents several environmental concerns, namely the risk of oil spill and the continuous emission of toxic compounds and particulates including black carbon, sulfur and para-aminohippuric acid (PAH).
Because HFO has high viscosity and is sticky, it is always heated by boiler steam for use in engines.
HFO designated as high-sulfur fuel oil (HSFO): 0.5% sulfur content 3.5%.
Due to environmental regulations, the use of HFO requires the installation of a scrubber device on the exhaust side of the engines (M/E and G/E) to reduce sulfur oxide (SOx) emissions.
Notes: Consistency: 농도
Residual: 남은, 잔여의
Remnant: 남은 부분
Aromatics: 방향성 물질
Predominantly: 대부분
Particulate: 입자성 물질

## Slide 8: Scrubber

## Slide 9: Marine fuels
VLSFO (Very Low Sulfur Fuel Oil):
VLSFO is a type of fuel oil with a sulfur content of 0.5% or less by weight.
The creation of VLSFO was primarily driven by the International Maritime Organization’s (IMO) regulation, known as IMO 2020, which mandated a hefty reduction in the sulfur content of ship fuels from 3.5% to 0.5% starting January 1, 2020.
This regulation aims to decrease the amount of sulfur oxide emissions from ships.
VLSFO has become the preferred choice for many due to its lower fuel cost compared to MGO and less complex implementation compared to fitting scrubbers.
Ultra Low Sulphur Fuel Oil (ULSFO) are fuels with a sulfur content not exceeding 0.10% S.

## Slide 10: Marine fuels
MDO (Marine Diesel Oil):
MDO is a type of fuel oil and is a blend of gasoil and HFO.
MDO is also called distillate marine diesel.
MDO does not need to be preheated before using, while HFO and VLSFO need to be preheated.
MGO is increasingly being used instead of MDO for use in areas (SECA: Sulfur Emission Control Area) subject to sulfur content regulations.

## Slide 11: Marine fuels
SECA: Sulfur Emission Control Area
0.1%

## Slide 12: Marine fuels
MGO (Marine Gas Oil):
MGO refers to marine fuels that consist solely of distillates, the components of crude oil that evaporate in fractional distillation and are then condensed from the gas phase into liquid fractions.
Distillates are all those components of crude oil that evaporate in fractional distillation and are then condensed from the gas phase into liquid fractions. MGO usually consists of a blend of various distillates.
MGO is similar to diesel but has a higher density, and unlike HFO, MGO doesn’t require heating during storage.
Notes: Fractional distillation: 분별 증류

## Slide 13: Marine fuels
LSMGO (Low Sulfur Marine Gas Oil):
MGO is produced with varying degrees of sulfur content, though the maximum permissible sulfur content of MGO lies below that of HFO.
LSMGO has a sulfur content of less than 0.1%.
This marine fuel can be used in EU ports or Emission Control Areas (ECAs), which among other things impose a sulfur emissions limit corresponding to that of LSMGO.
For this reason, most shipping companies use a LSMGO in these places.

## Slide 14: Marine fuels
How is marine fuel loaded onto a ship? (This is called bunkering)
1) Bunker Barge (Most ships receive their fuel from bunker barges
to load large quantities of fuel onto the ship.)
Hose from bunker barge
Bunkering manifold
Bunker barge
Bulk carrier
Bunker barge
Container ship

## Slide 15: Marine fuels
How is marine fuel loaded onto a ship?
2) Tank Lorry (Tank lorries can be used when supplying MGO to ships in small quantities. However, in most cases, all fuel is supplied by bunker barges. Tank Lorries are mostly used to supply lubricants.)

## Slide 17
Fuel supplied from the bunker barge is stored in oil storage tanks (H.F.O. tank or M.G.O tank) from the bunker manifold.
: F.O.
: M.G.O.

## Slide 18
The oil in the H.F.O. tank is sent to the H.F.O. settling tank by the H.F.O. transfer pump.
: F.O.

## Slide 19: Drain for F.O. tanks
Since sludge and water accumulate at the bottom of every FO tank, apprentice engineers usually drain it twice a day.

## Slide 20
The oil in the H.F.O. sett. tank is purified by the H.F.O. purifier and then sent to the H.F.O. serv. tank.
: H.F.O.
: L.S.H.F.O.
: Common

## Slide 21
Since MGO does not need to be purified, it is sent from the M.G.O. stor. tank to the M.G.O. serv. tank by the M.G.O. trans. pump.

## Slide 23
HFO or LSHFO reaches the G/E inlet from the
1) service tank through the
2) G/E F.O. supply pump,
3) Flowmeter,
4) G/E F.O. booster pump,
5) G/E F.O. heater, 6) Viscorator,
7) G/E F.O. auto back-flushing filter.
: H.F.O.
: L.S.H.F.O.
: Common

## Slide 24
: M.G.O.
MGO reaches the G/E inlet from the
1) service tank through the
2) G/E F.O. supply pump,
3) Flowmeter,
4) G/E M.G.O. cooler,
5) G/E F.O. booster pump.
(G/E F.O. auto back-flushing filter is turned off or by-passed.)

## Slide 25
MGO reaches the G/E inlet from the 1) service tank through the
2) G/E M.G.O. flushing pump.
When using a G/E M.G.O. flushing pump, the purpose is to flush only the specific G/E with M.G.O. for reasons such as long-term maintenance, while other G/Es are operated with H.F.O.
: M.G.O.

## Slide 26
Internal Fuel Oil System for G/E (MAN B&W)

## Slide 27
The oil that reaches the G/E inlet is pressurized by the engine driven fuel oil feed pump and then passes through the fuel oil filter to reach the fuel oil pump.
(The fuel oil filter is also called as “duplex filter/strainer”.)
Internal Fuel Oil System for G/E (MAN B&W)
Fuel oil filter

## Slide 28
The fuel oil feed pump is not installed in the HiMSEN engine.
Diagram for the internal fuel oil system for G/E (HiMSEN)

## Slide 29: Fuel injection pump (MAN B&W)
The photos below are actual photos of the
fuel injection pump taken from various angles.

## Slide 30: Fuel injection pump (MAN B&W)
YouTube videos can be useful for understanding the structure of fuel injection pumps.
Various videos are available on YouTube, so please search for them.

## Slide 31: Fuel injection pump (MAN B&W)

## Slide 32: Fuel injection pump (MAN B&W)

## Slide 33: Fuel injection pump (MAN B&W)

## Slide 34: Fuel injection pump (HiMSEN)
The fuel injection pump of the HiMSEN engine is much larger (also heavy) and looks slightly different than the fuel injection pump of the MAN B&W, but the operating mechanism is the same.
YouTube can be referenced to understand the fuel injection pump of the HiMSEN engine.

## Slide 35: Fuel injection pump (HiMSEN)

## Slide 36: Fuel injection pump (HiMSEN)

## Slide 37: Fuel injection pump (HiMSEN)
The fuel injection pump is installed above the camshaft, and it is activated by the cam on the camshaft.
Camshaft
Crank
shaft

## Slide 38: Fuel injection pump (HiMSEN)
The fuel injection pump is installed above the camshaft, and it is activated by the cam on the camshaft.

## Slide 39: Fuel injection pump (HiMSEN)
The fuel injection pump is installed above the camshaft,
and it is activated by the cam on the camshaft.
Cam for fuel injection pump
Cam for rocker arm
Fuel injection pump
Cam for fuel injection pump
Camshaft
The camshaft piece can be disassembled to replace the camshaft itself or the bearing shells for the camshaft.

## Slide 40: Camshaft (HiMSEN)

## Slide 41: Fuel injection pump (HiMSEN)
Plunger
Barrel
Rack (also called as fuel rack)
Sleeve

## Slide 42: Fuel injection pump (MAN B&W)
The fuel injection pump is installed on the roller guide housing directly above the camshaft, and it is activated by the cam on the camshaft through roller guides fitted in the roller guide housing.
Roller
Roller guide
Roller guide for
fuel injection pump
Roller guide for
valve gear (Not for this chapter)
Cam for fuel injection pump

## Slide 43: Fuel injection pump (MAN B&W)
Plunger
Barrel
Regulating rod
Gear rim

## Slide 44: Fuel injection pump
The injection amount of the pump is regulated by transversal displacement of a toothed rack in the side of the pump housing. The plunger, which is fixed to the gear rim, rotates as the regulating rod (fuel rack) moves back and forth. As the plunger rotates, the amount of oil flowing out through the spillport changes, and accordingly, the amount of pressurized oil flowing to the outlet (to the high pressure pipe then fuel injection valve) changes.
Notes: Transversal : 횡단하는
Displacement : 이동

## Slide 45: Fuel injection pump
The plunger performs reciprocating motion by the cam on the camshaft.
Inlet
Spillport
Outlet to high pressure pipe and fuel injection valve

## Slide 46: Fuel injection pump

## Slide 47: Fuel injection pump (HiMSEN)
Adjustment of fuel injection timing
Fuel injection timing influences the maximum cylinder pressure which is set properly by engine maker and normally recommended not to be adjusted.
However, if new fuel injection pump has been installed or if the deviation of each cylinder pressure is out of tolerance, the injection timing should be checked and adjusted, which can be adjusted by the thickness of thrust plate as shown in fig 1.
When inserting thrust plate (increasing thickness), the injection timing advanced and maximum cylinder pressure increased.
Thrust plate thickness + 0.1mm = Cyl. pressure + 2 bar

## Slide 48: Fuel injection pump (HiMSEN) & Govenor
The fuel racks of all fuel injection pumps are connected to a common regulating shaft and spring-loaded linkages.
Governor
Fuel injection pump
Fuel rack
Fuel rack
Governor
linkage
assembly

## Slide 49: Govenor

## Slide 50: Fuel injection pump (HiMSEN) & Govenor
Depending on the fuel injection pump, fuel may not be injected into the cylinder when the fuel rack is pulled in, or fuel may not be injected into the cylinder when the fuel rack is pushed in.

## Slide 51: Fuel injection pump & Govenor
Governor

## Slide 52: Fuel injection pump & Govenor
Fuel injection pump
Fuel rack

## Slide 53: Fuel injection pump & Govenor

## Slide 54: Fuel injection pump & Govenor

## Slide 55: Fuel injection pump (HiMSEN) & Govenor
Engine Stop System
The engine is stopped when pressing ‘STOP’ button or ‘EMERGENCY STOP’ button on control panel intentionally, or by ‘AUTO STOP’ signal.
Engine automation system generate ‘AUTO STOP’ signal when abnormal condition of the engine is detected.
However, the engine is stopped fundamentally when the fuel injection into the combustion chamber is stopped. This means that the rack of each fuel injection pump is moved to stop position by stop signal. Every fuel rack is connected to common control shaft mechanically and also connected to common compressed air line pneumatically.

## Slide 56: Fuel injection pump (HiMSEN) & Govenor
Engine Stop System
Therefore, there are two ways of moving fuel racks to stop position (Zero index) as shown in fig 2.
The one is by the mechanical stop, which pull the racks to stop position by the governor or the manual control lever. ‘STOP’ button activates the governor to be ‘STOP’ position.
The other is by the pneumatic stop by compressed air, which pushes the rack to stop position regardless of the governor control. ‘EMERGENCY STOP’ button or ‘AUTO STOP’ signals activates the stop solenoid valve to supply the compressed air for all fuel injection pumps. This ‘EMERGENCY STOP’ signal also activates governor’s stop simultaneously.

## Slide 57: Lambda cylinder
Lambda cylinder
lambda cylinder is located near the governor linkage assembly and prevents excessive fuel from being injected into the cylinder during G/E initial start.
When the G/E overspeeds, compressed air is sent to the lambda cylinder, which in turn restricts the fuel rack connected to the linkage assembly, thereby restricting fuel injection into the cylinder and preventing overspeed.

## Slide 58: Overspeed device (just for reference)

## Slide 59: Overspeed device (just for reference)

## Slide 60: Lambda cylinder
Lambda cylinder
lambda cylinder is located near the governor linkage assembly and prevents excessive fuel from being injected into the cylinder during G/E initial start.
When the G/E overspeeds, compressed air is sent to the lambda cylinder, which in turn restricts the fuel rack connected to the linkage assembly, thereby restricting fuel injection into the cylinder and preventing overspeed.

## Slide 61: Lambda cylinder
Lambda cylinder
As the load on the G/E increases, the pressure of the charging air increases, overcoming the spring force and lifting the piston, releasing the fuel injection restriction of the fuel rack.

## Slide 62: Lambda cylinder
Lambda cylinder
The purpose with the lambda controller is to prevent injection of more fuel in the combustion chamber of an auxiliary engine on the ship, than can be burned during a momentary load increase. This is carried out by controlling the relation between the fuel index and the charge air pressure.
The Lambda controller is also used as stop cylinder.
Advantages of Lambda Controller
The lambda controller has the following advantages:
Reduction of visible smoke in case of sudden momentary load increases on auxiliary engines.
Improved load ability.
Less fouling of the engine’s exhaust gas ways.
Limitation of fuel oil index during starting procedure.

## Slide 63: Lambda cylinder
Principle of Lambda Controller
In case of a momentary load increase, the regulating device will increase the index on the injection pumps and hereby the regulator arm (1) is turned, the switch (2) will touch the piston arm (3) and be pushed downwards, whereby the electrical circuit will be closed.
Thus, the solenoid valve (4) opens. The jet system is activated, the turbocharger accelerates and increases the charge air pressure, thereby pressing the piston (3) backwards in the lambda cylinder (5). When the lambda ratio is satisfactory, the jet system will be deactivated.
At a 50% load change the system will be activated for about 3-8 seconds.
If the system is activated more than 10 seconds, the solenoid valve will be shut off and there will be a remote signal alarm for “jet system failure”.

## Slide 64: Lambda cylinder
Fuel oil limiting during start procedure
During the start procedure the lambda controller is used as an index limiter.
Hereby heavy smoke formation is prevented during start procedure and further the regulating device cannot over-react.
The jet system is blocked during the starting procedure until the engine has reached about 110 RPM.

## Slide 65: Lambda cylinder

## Slide 66: Lambda cylinder

## Slide 67: Lambda cylinder

## Slide 68: Fuel rack limiter ( Lambda cylinder)

## Slide 69: Fuel rack limiter ( Lambda cylinder)
During starting period, the turbocharger is out of normal operation and therefore diesel engine is always in the incomplete combustion due to lack of air, which results in heavy smoke.
Digital governors have fuel limiting function for starting, while hydraulic governor normally has not.
However, the engine has adjustable fuel limiter for starting period regardless of the governor type.

## Slide 70: Fuel rack limiter ( Lambda cylinder)
The fuel limiter piston is used for starting limiter to avoid excessive fuel injected into cylinder during starting period to avoid heavy smoke.
During starting period, the engine automation system activate starting solenoid valve to supply compressed air to push the fuel limiter piston as shown in fig 5.

## Slide 71: Fuel rack limiter ( Lambda cylinder)
Fuel rack limiter

## Slide 72: Govenor
Most of the governors installed in G/E use Woodward products.
Woodward hydraulic-mechanical and electronic governors provide reliable and precise control of engine speed and output in every type of engine application.
The main purpose of the governor is to control the amount of oil injected into the engine cylinder by adjusting the fuel rack of the fuel injection pump connected to the governor linkage assembly to maintain a constant RPM of the G/E.

## Slide 73: Fuel oil high pressure pipe
The connection between injection pump and fuel injector is a shielded high pressure pipe. The high pressure pipe is equipped with connection tapers matching to similar taper facings on the threaded connectors on the injection pump and the fuel injector.
Fuel injection pump
Fuel oil high
pressure pipe
Fuel oil high pressure pipe is connected to the fuel injection valve
Fuel injection valve
Fuel oil high pressure pipe is connected to the fuel injection pump

## Slide 74: Fuel oil high pressure pipe
Fuel oil high
pressure pipe
Fuel injection pump
Cylinder head

## Slide 75: Fuel oil high pressure pipe (HiMSEN)
Fuel oil high
pressure pipe
Fuel injection pump
Cylinder head
The fuel oil high pressure pipe of the HiMSEN engine is different from that of other brands of G/E.

## Slide 76: Fuel oil high pressure pipe (HiMSEN)

## Slide 77: Fuel oil high pressure pipe (HiMSEN)

## Slide 78: Fuel oil high pressure pipe (HiMSEN)

## Slide 79: Fuel injection valve
The fuel injection valve (FIV) is a component that injects atomized fuel into the cylinder.
The FIV is mounted on the cylinder head and connected to the fuel oil high pressure pipe, receives pressurized fuel oil from the fuel injection pump, and injects atomized fuel.

## Slide 80: Fuel injection valve
The fuel injection valve (FIV) is inserted into the hole below.

## Slide 81: Fuel injection valve (MAN B&W)

## Slide 82: Fuel injection valve (HiMSEN)

## Slide 83: Fuel injection valve (HiMSEN)

## Slide 84: Fuel injection valve (HiMSEN)
Valve opening pressure : 450 bar

## Slide 85: Fuel injection valve (HiMSEN)
Checking Atomizing Condition
1. Checking procedure
1) Actuate the hand pump evenly until the pressure gauge shows 250 bars.
2) The injection nozzle can be considered tight if no drop falls within a period of 5 seconds.
2. Criterion of decision – All nozzle holes open
1) Keeping the tightness: normal
2) Dripping on nozzle: re-conditioning or changing to a new one.

## Slide 86: Fuel injection valve
Pressurized fuel entering the FIV overcomes the spring force and lifts the needle of the nozzle, spraying it through several tiny holes and ultimately injecting atomized fuel into the cylinder.

## Slide 87: Fuel injection valve

## Slide 88: Fuel injection valve

## Slide 89: References
1) https://en.wikipedia.org/wiki/Heavy_fuel_oil
2) https://lubmarine.totalenergies.com/faq/glossary/heavy-fuel-oil-hfo
3) https://www.bbc.co.uk/bitesize/guides/zgx2k2p/revision/4
4) https://anchinv.com/oil-refining-and-petrochemical-industry-overview/
5) https://www.vesselfinder.com/vessels/details/9332810
6) https://www.freepik.com/premium-photo/cropped-hand-person-with-crude-oil_124527185.htm
7) https://en.yna.co.kr/view/AEN20221007009700320
8) https://www.kedglobal.com/earnings/newsView/ked202108090018

## Slide 90: References
9) https://www.alfalaval.com/industries/marine-transportation/marine/fuel-oil-treatment/fuel-line/marine-fuels-in-the-low-sulphur-era/
10) https://www.ics-shipping.org/wp-content/uploads/2022/09/MEPC-79-5-Sulphur-content-in-Very-Low-Sulphur-Fuel-Oil-VLSFO-and-examples-of-geographical-differen...-ICS-BIMCO-INTERTANKO-an....pdf
11) https://msp.energy/whats-that-very-low-sulfur-fuel-oil-vlsfo/
12) https://www.researchgate.net/figure/Comparison-of-manufactured-samples-with-marine-fuel-oils-a-heavy-fuel-oil-b-marine_fig3_385853486
13) https://danalubes.com/marine-diesel-oil/?srsltid=AfmBOooWJzXQubzGZBJWYdzf4Ts8nB5p9BBefeteEi47dFHlGXp5rjdf
14) https://www.researchgate.net/figure/Map-and-requirements-of-the-Emission-Control-Areas_fig1_314469733

## Slide 91: References
15) https://www.researchgate.net/figure/Comparison-of-marine-fuel-oil-samples-a-gasoline-oil-b-diesel-oil-c-kerosene_fig4_369250898
16) https://www.sciencedirect.com/science/article/pii/S0016236121012023
17) https://www.nedmag.com/markets-and-applications/environment/marine-scrubbers
18) https://livebunkers.com/what-bunker-ship-about-bunker-fuel-and-bunkering-procedure
19) https://www.seably.com/courses/bunkering-and-vlsfo/lessons
20) https://www.iims.org.uk/lessons-learnt-bunker-fuel-contamination-incident-highlighted-uk-pi-club/
21) https://www.bluebird-electric.net/bunkers_fuel_coal_oil_diesel_energy.htm

## Slide 92: References
22) https://www.researchgate.net/figure/Bunkering-methods-Figure-4_fig1_347099136
23) https://marineinfo.com/fuel-oil-purifier-system/
24) https://marineinfo.com/auxiliary-engine-fuel-oil-supply-system/
25) https://korean.fh-marine.com/sale-45955895-shipbuilding-duplex-oil-filter-double-oil-filter-as16040-cb-t425-94-straight-type-cast-iron-body-wit.html
26) https://trusttrading.en.made-in-china.com/product/xdmJnQNjsfVK/China-Marine-Duplex-Fuel-Oil-Filter-for-Maine-Engine.html
27) https://www.industrialmarinepower.com/fuel-pump-for-man-bw-l-2330-h-19081/
28) https://spare-parts.injegov.gr/product/man-bw-23-30h-fuel-pump/
29) https://www.youtube.com/watch?v=fsD0dzCw-Qc

## Slide 93: References
30) https://makeagif.com/gif/fuel-injection-pump-animation-uOjU9B
31) https://www.mdpi.com/2071-1050/15/11/8948
32) https://makeagif.com/gif/jerk-type-or-plunger-type-fuel-injection-pump-working-and-animation-4Lp3o3
33) https://makeagif.com/gif/jerk-type-or-plunger-type-fuel-injection-pump-working-and-animation-I0Zhzf
34) https://www.youtube.com/watch?v=w9jMvJZwRuE
35) https://www.youtube.com/watch?v=eA5qipliN9w
36) https://www.oldtimerengines.com.au/bpf1-fuel-injection-pump-assembly
37) https://www.heinzmann.com/en/application-areas/marine-engine-controls
38) https://marineengineering101.wordpress.com/2023/05/05/how-the-governor-functions-auxiliary-engine-edition/

## Slide 94: References
39) https://www.youtube.com/watch?v=BmfQMHXejuU
40) https://www.google.com/imgres?imgurl=https%3A%2F%2Fmarineengineering101.wordpress.com%2Fwp-content%2Fuploads%2F2023%2F04%2Fimg202304160220474306236060561681909.jpg%3Fw%3D768&tbnid=rpMZ0hCqVcrzIM&vet=10CBIQxiAoCGoXChMI2PjaurugjwMVAAAAAB0AAAAAEA4..i&imgrefurl=https%3A%2F%2Fmarineengineering101.wordpress.com%2F2023%2F05%2F05%2Fhow-the-governor-functions-auxiliary-engine-edition%2F&docid=EkoswDz4ad5qrM&w=768&h=1024&itg=1&q=ship%2C%20governor%2C%20woodward&ved=0CBIQxiAoCGoXChMI2PjaurugjwMVAAAAAB0AAAAAEA4#imgrc=ibOkHjWlCoMTiM&imgdii=35BcLiPsrvIPoM
41) https://www.woodward.com/products/industrial/hydraulic-mechanical-governors/
42) https://www.youtube.com/watch?v=BnI3NfHrAVw
43) https://www.marinesite.info/2013/09/fuel-injector.html#google_vignette
44) https://www.youtube.com/watch?v=BnI3NfHrAVw
45) https://www.youtube.com/watch?v=r34lcLQDjEM
46) https://marinengcalc.blogspot.com/2018/05/calculation-of-fo-settling-tank.html

## Slide 95: References
47) https://www.hiseastocks.com/products/JIS-F7398-25A-Oil-Tank-Self-Closing-Drain-Valve.html
48) https://www.jinbomarine.com/marine-bronze-fuel-oil-tank-self-closing-drain-valve-jis-f7398u-5k.html
49) https://www.youtube.com/watch?v=oI-AYvdRCY4
50) https://www.meoexamnotes.in/2020/01/lambda-controller.html
51) https://shipsparesindia.com/product/man-bw-23-30-injector/